WINTERIZING YOUR IN-GROUND POOL

In order to insure a clean pool in the spring, first vacuum the pool to remove all debris.  Secondly, do not winterize your pool until late September or early October.

# Step 1 	Make sure that the pool is not leaking.  If it is leaking, repair the leak before winterizing or there will be severe and expensive damage to the pool if not fixed.

Step 2		Vacuum the pool completely to remove all debris.

Step 3	Balance water chemistry before winterizing the pool.  Make sure the pH is 7.2-7.6 and Total Alkalinity is 80-120 ppm.  Failure to do so can result in premature failure of the liner.

Step 4	Add winterizing chemical to allow proper mixing of chemicals.

Recommended dosages (Chlorine pools only):

| 10,000-15,000 gallons | 15,000-25,000 gallons | 25,000-30,000 gallons |
| --- | --- | --- |
| 4 gal. Shock | 5 gal. Shock | 6 gal. Shock |
| 1 qt. 60% Algicide |  |  |